## Slide 1: Cyclone science and improving product recovery in spray drying (SD) processes
Romualdo Salcedo
CTO, Advanced Cyclone Systems
Professor, ChemEngDep, University of Porto
April 13th, 2016
University of Leeds

## Slide 2: Why are cyclones important in SD?
DISADVANTAGES OF LEGACY SOLUTIONS:
HE Cyclones:
Low efficiency for fine particles
Bag Filters:
Product degradation
Product contamination
Production downtime
Cleaning costs
Cyclones are the best devices
for high quality product recovery
Because they are the best collectors for first-grade product recovery

## Slide 3: Several constraints are imposed on design
Wide range of operating conditions:
…- 85ºC < T < 120ºC (negative T for cryogenic micronizers)
…mg/Nm3 < C_in < …kg/Nm3 (highest values occur with jet mill micronizers)
…25 Nm3/h < Q < …150,000 Nm3/h (highest flowrates occur with quasi-pharma applications, e.g., food ingredients)
Type of product:
…solid dispersions, inhalable, injectable, microcapsules, tablets’ waste recovery, …
…wide range of densities (non-porous, porous)
This makes it very difficult to have a single cyclone geometry to effectively deal with all cases

## Slide 4: Particle size distributions in SD
Very Fine
Fine
Coarse
Medium

## Slide 5: How can we design better cyclones?
The cyclone geometry is defined by 7 dimensionless ratios of its 8 independent dimensions to the cyclone D
To optimize the geometry becomes a problem with 7 degrees of freedom, usually non-linear and non-convex
A 2-level factorial design would require building 128 prototypes and a 4-level, 16384……

## Slide 6
Setting up a mathematic problem
Equality constrains
Relevant design équations (cyclone modeling)
Particle size distribution and density
Gas flow rate and dust load
Gas temperature, density and viscosity
Solution:
Numerically optimized cyclones
Inequality constrains
Maximum pressure loss
Saltation velocity
Geometric constraints
Maximize efficiency, conditioned to:
Advanced Cyclone Systems | www.acsystems.pt

## Slide 7: The solution
  We have abandoned pure empiricism and resorted to mathematical programming
Use empiricism only to test and possibly improve the numerical solution, found among thousands of virtual prototypes
But first, one has to understand how cyclones work…cyclones are deceptively simple

## Slide 8: Cyclone dynamics
Effect of operating conditions
(P, T, PSD)
Effect of multiphase flow
(inlet concentration, particle density and porosity, …)
Possible clustering and strand formation (Muschelknautz)
Highly vorticial asymmetric turbulent flow field
CFD only in 2015 used for global optimization

## Slide 9: How to proceed?
Find an appropriate collection model - neglect particle-particle interaction
Superimpose particle-particle interaction
Optimize using a global optimizer - stochastic is slower but much better at obtaining the global optimum (Salcedo, 1992)
Build and test the numerical solution

## Slide 10: 1. Find an appropriate collection model
The Mothes and Loffler model (1988) seems to best describe the collection of particles by cyclones, neglecting particle-particle interaction (Clift et al., 1991)
Problem: this model depends on the particle turbulent diffusivity, that depends on cyclone operating conditions, particle size distribution and cyclone geometry (Salcedo and Coelho, 1999)
With the above approach, the line of Hurricane (HR) cyclones has been developed and patented (EP0972572A2)

## Slide 11
Technology: Hurricane
Application: Caseinate/Hydrolisate recovery
Dimension: 92,140 am3/h
Client: Arla Foods
Location: Denmark
Load into Cyclone: 17 g/Nm3
Hurricane Efficiency: 98.9-99.3 %
Alternative technology: Competitor HE cyclone
Alternative Cyclone Efficiency: 96 %
Increased Recovered Powder: 320 ton/year
Reduction in losses: 77%
HR performance in SD applications

## Slide 12
Project 1:
1,500 kg/h (N2) @ 85ºC
Measured on HR: 96%
Competing cyclone: 83%. Reduction in losses: 76%
Project 2:
80 kg/h (N2) @ 65ºC
Measured on HR: 85-95%
Competing cyclone: 80-90%. Reduction in losses: 25-50%
Project 3:
112 kg/h (N2) @ 65ºC
Measured on HR: 84%
Competing cyclone: 60%. Reduction in losses: 60%
Project 4:
1250 kg/h (N2) @ 85ºC
Measured on HR: 99.7%
Competing cyclone: 97%. Reduction in losses: 90%
Some Pharma results on HR performance
from leader API manufacturer

## Slide 13: 2. Superimpose particle-particle interaction
?
Mothes and Loffler (1988)
From D =20 mm
Grade-Efficiency at Lab Scale
Abnormal capture of fine particles - Why?

## Slide 14
ML (1988)
...to D =1200 mm
Grade-Efficiency at Industrial Scale

## Slide 15: Schematics of particle-particle collisions
Trajectories
Agglomerate Formation

## Slide 16: Clustering (based on Ho and Sommerfeld, 2002)

## Slide 17: Main Model Equations (PACyc)
Particle Trajectory
Introducing Turbulence in the Fluid
New Class-Efficiency (after History Rebuild)

## Slide 18: Effect of maximum collision (target) diameter

## Slide 19
Effect of inlet concentration
_____ ML (not sensitive to C_in)
7 mg/m3
70 mg/m3
700 mg/m3

## Slide 20: Effect of residence time
REF: p=1450 kg.m-3
Dmax = 6 µm
tmax = 10 ms
Cin = 700 mg.m-3

## Slide 21
ML (1988)
PACyc (2010)
Very good agreement with experimental data

## Slide 22
  We have extended the ML (1988) and Ho and Sommerfeld (2002) models to predict fine particle clustering in turbulent cyclone flows
  Fair agreement between experimentally observed grade-efficiency curves and those from our model
  Excellent agreement between predicted and experimental global collection efficiency
  There is now a theoretical framework on which to base our hyphothesis, viz. that clustering inside the cyclone may be responsible for the very high collection of fine particles
PACyc conclusions

## Slide 23: 3. Optimize with the PACyc model

## Slide 24
The outcome: the Hurricane_MK
Under patent pending (PTC 107312), it shares no more than 2 ratios with
≈ 190 geometries available in the scientific literature or in the marketplace
Projections for difficult API (rp=450 kg/m3):
HR; 57%
HR_MK; 76%
Projections confirmed by client: Reduction in losses 44%

## Slide 25: Grade-efficiencies including clustering
Fig. 1 - Particle size distribution reconstructed from cyclone (42%), filter (53%) and losses (5%).
Fig. 2 - Grade and global efficiencies from competing cyclone (experimental) and predicted by PACYC for HR and HR_MK cyclones
(particle density; 711 kg/m3)
HR130; MK250

## Slide 26
Pilot-scale test conditions

## Slide 27
Sample – fine fly ash inlet PSD

## Slide 28
Sample – grade efficiencies
Increased concentration
(121, 363, 1231 mg/m3)
PACyc @ 572 mg/m3

## Slide 29
Sample – global efficiencies

## Slide 30
Industrial-scale test conditions
(24x1050mm HR_MK)

## Slide 31: What about CFD? (Sgrott et al., 2015)

## Slide 32: Scaling is no problem
1x10mm hydrocyclone for mamalian cell separation
4x3750mm cyclones for ferrous industry (600,000 m3/h)

## Slide 33: Conclusions
Global optimization with a good simulation (PACyc) is a powerfull weapon to design better cyclones
Taylor-made cyclones can be designed to meet specific demands
Different simulation packages will obtain different ‘optimum’ solutions
The numerical solutions have to be throughly tested before implementation
ACS has gained a good confidence on its cyclone design methodology
Which is the better cyclone will depend partly on the operating conditions and mostly on particle properties (density, porosity and particle size distribution).

## Slide 34: References
Alves, A., J. Paiva and R. Salcedo, Cyclone optimization including particle clustering, Powder Technology vol. 272, 14-22, 2015.
Ho, C. A. and M. Sommerfeld, Modelling of micro-particle agglomeration in turbulent flows, Chemical Engineering Science, vol. 57, 3073-3084, 2002.
Clift, R., M. Ghadiri and A. C. Hoffman, A critique of two models for cyclone performance, AIChE J., vol. 37 (2), 1991.
Sgrott, O.L., Noriler D., Wiggers, V.R. and Meier, H.F., ‘Cyclone optimization by COMPLEX method and CFD simulation’, Powder Technology, vol. 277, 11-21, 2015.
Paiva,J., R. Salcedo and P. Araujo, Impact of particle agglomeration in cyclones, Chem. Eng. J., vol. 162, 861-876, 2010.
Mothes, H. and F. Loffler, ‘Prediction of particle removal in cyclone separators’, International Chemical Engineering, vol. 28, 231-240, 1989.
Salcedo, R. L., ‘Solving Non-Convex NLP and MINLP Problems with Adaptive Random-Search’, Ind. Eng. Chem. Res., vol. 31, no.1, 262-273, 1992.
Salcedo, R. and Coelho, M., ‘Turbulent dispersion coefficients in cyclone flow – an empirical approach’, Can. J. Chem. Eng., vol. 77, 609-617, 1999.
Salcedo, R. L., High efficiency cyclones, EP0972572A2, European Patent Application 99670006.8, Bulletin 2000103, January 19, 2000 (granted).
Salcedo, R. and J. Paiva, Reverse flow agglomerating cyclone and process thereof, PTC 107312, INPI, November 25, 2013 (pending).

## Slide 35: Thank you contacts: technical@acsystems.pt