## Slide 1: Vehicle Refueling Emissions
Refueling Emission Inventories and Regulatory Policy
US EPA Emissions Inventory Conference Baltimore, MD
August 2017
Glenn W. Passavant Ingevity Corporation North Charleston, SC

## Slide 2: Overview
What are vehicle refueling emissions?
What hydrocarbon compounds are in refueling emissions?
Why should we care about refueling emissions?
What factors affect the per vehicle refueling emission rate?
Case 1: USA
Case 2: China
Case 3: EU
Case 4: Brazil
2

## Slide 3: What are vehicle refueling emissions?
VOC vapor and entrained droplets displaced from the fuel tank ullage.
Any fuel spilled during the refueling event.
3
.
Mostly of concern for volatile liquid fuels (>2 psi RVP)

## Slide 4: VOC Composition of Refueling Emissions
Refueling vapors are dominated by (C4 and C5) compounds (butanes and pentanes); liquid gasoline is dominated by a variety of heavier (C6 to C9) compounds.
Addition of ethanol changes vapor composition but it remains dominated by lighter weight compounds (C5 or less).
4
0
10
20
30
40
50
60
70
C3
C4
C5
C6 C7
C8
C9
C10
C11
Percent of Total
Carbon Number
fuel vapor
SAE Paper 880712 : “Factors Influencing the Composition and Quantity of Passenger Car Refueling Emissions ‐ Part II”

## Slide 5: Why Control Refueling Emissions? – O3 Reactivity
mass % mass % CA ARB mass vapor
Ozone is formed through photochemical interactions of VOCs and NOx. Many different VOCs are emitted into the atmosphere, each reacting at different rates and with different reaction mechanisms.
The differences in rates of ozone formation are referred to as the ozone "reactivity" of the VOCs and are quantified through Reactivity Adjustment Factors (RAFs).
Ozone RAFs have been determined for each VOC.
The lighter weight compounds which are dominant in gasoline vapor are moderately reactive. However, they represent such a large fraction of the total emission mass, that reducing lighter ends through RVP control is a major ozone reduction strategy.
In this sample, C4‐C5 compounds represent 65% of ozone forming potential emissions from gasoline vapor.
VOCs, such as aromatic compounds. also form secondary organic aerosols (PM 2.5). The fraction of aromatic compounds varies with gasoline grade.
* SAE Paper 860086: “Composition of Vapor Emitted from a Vehicle Gasoline Tank During Refueling”
** 17 CCR 94700 : “Maximum Incremental Reactivity Values for Compounds ‐ 2010”
Compound | liquid* | vapor* | RAF** | % wtd RAF
propane | 0.06 | 1.9 | 0.49 | 0.65%
n‐butane | 5.27 | 47.6 | 1.15 | 38.30%
n‐pentane | 1.21 | 3.1 | 1.31 | 2.84%
n‐hexane | 1.28 | 0.9 | 1.15 | 0.72%
isobutane | 0.45 | 6.1 | 1.23 | 5.25%
isopentane | 4.92 | 17.6 | 1.45 | 17.86%
2,2‐dimethylbutane | 0.01 | 0.7 | 1.17 | 0.57%
2,3‐dimethylbutane | 2.2 | 2.6 | 0.97 | 1.76%
2‐methylpentane | 1.81 | 1.9 | 1.5 | 1.99%
3‐methylpentane | 1.28 | 1.2 | 1.8 | 1.51%
2,4‐dimethylpentane | 1.78 | 0.9 | 1.55 | 0.98%
3,3‐dimethylpentane | 3.79 | 1.2 | 1.2 | 1.01%
3‐methylhexane | 1.3 | 0.4 | 1.61 | 0.45%
2,2,4‐trimethylpentane | 9.12 | 2.2 | 1.2 | 1.85%
2,3,4‐trimethylpentane | 5.41 | 0.7 | 0.96 | 0.47%
methylcyclopentane | 0.47 | 0.3 | 2.06 | 0.43%
2‐methyl‐1‐butene | 0.16 | 0.5 | 6.4 | 2.24%
cis‐2‐butene | 0.07 | 0.5 | 14.24 | 4.98%
trans‐2‐butene | 0.03 | 0.5 | 15.16 | 5.30%
cis‐2‐pentene | 0.21 | 0.5 | 10.38 | 3.63%
toluene | 18.01 | 2.3 | 4 | 6.44%
benzene | 2.9 | 1.5 | 0.72 | 0.76%
5

## Slide 6: Air Toxic Exposures
Gasoline vapor contains compounds which adversely affect health
Occupational health impacts for service station attendants:
  At higher concentrations, gasoline vapor may result in adverse impacts
    Symptoms: irritant, dermatitis, headache, lassitude, blurred vision, dizziness, slurred speech, confusion, convulsions; chemical pneumonitis; possible liver, kidney damage
  ACGIH 8‐hr gasoline vapor TLV is 300 ppm and the 15‐min.; STEL is 500 ppm.
  Even at very low concentrations, benzene vapor may result in adverse impacts
    Hematotoxicity and potential carcinogen (leukemia)
  ACGIH 8‐hr benzene TLV is 0.50 ppm and the 15‐min. STEL is 2.5 ppm.
Community health impacts
  No identified chronic exposure standards for gasoline vapor or benzene, only AEGLs.
B. Edokpolo, Q.J. Yu, D. Connell, “Health Risk Characterization for Exposure to Benzene in Service Stations and Petroleum Refineries Environments Using Human Adverse Response Data,” Toxicology Reports 2 (2015), pp. 917‐927.
6

## Slide 7: Refueling VOC Emission Rates
Between 1972 and 1988 there were at least six studies which evaluated uncontrolled refueling emission rates on a g/gal basis.
Each study gave a slightly different results depending on the vehicles evaluated and the range of the key experimental factors included such as the vapor pressure and temperatures.
A 1988 study by the CRC (VE‐6) was the most comprehensive. The relationship in the equation below reflects a fill from 10% to 100%. It is the equation used by EPA.
Where ∆T = (Ttank‐Tdispensed ); temperatures are in F, RVP is in psi
g/gal = exp[‐1.2798‐0.0049(∆T) + 0.0203(Td) + 0.1315(RVP)]
7

## Slide 8: Factors Affecting the VOC Emission Rate
Three primary factors:
  Reid vapor pressure (RVP) of fuels
  Dispensed fuel temperature Td
Tank fuel temperature T
t
Several secondary factors:
  Dispensing rate
  Tank and fillpipe configuration
  Initial volume of fuel in tank and volume dispensed
Ethanol/methanol blends affect RVP. RVP control is needed.
0
2
4
6
10
12
14
RVP (psi)
0 2.5 5 7 10 15 20 30 50 70 90 100
% Alcohol
Methanol Ethanol
M15
E10
8
SAE Paper 852116, “Volatility Characteristics of Gasoline‐Alcohol and Gasoline‐Ether Fuel Blends”.
7

## Slide 9: Benzene Refueling Emission Rate
Largely dependent on volume % benzene in liquid fuel. (mass % = 0.85 vol %)
HOWARD E. RUNION (1975) Benzene in Gasoline, American Industrial Hygiene Association Journal, 36:5, 338‐350
vol% Bz vapor = 0.43*(vol % Bz liquid)
* See SAE Paper 861559: Factors Influencing Benzene Emissions from Passenger Cart Refueling, October 1986.
9
Observations
Based on headspace equilibrium measurements, 1% benzene in liquid yields 0.43% in vapor or 4300 ppmv.
At STP, this converts to 13737 mg/m3 or about 0.05 g benzene/gallon.
Limited data from vehicle testing suggests that benzene emission rate is also affected by any entrained droplets and vapor shrinkage or growth.*
Bz (g/gal) = 0.052 (vol% Bz liquid)

## Slide 10: Spillage
Spillage is generally divided into four categories.
  Pre‐fill nozzle handling by the operator
  Pre‐mature shut‐off spit back
  End of fill event well back and topping off
  Post‐fill nozzle handling by the operator
SAE 720931: An Investigation of Passenger Car Refueling Losses
1 ml spilled gasoline is about 0.7 g of VOC. Even a “drop” is about 0.05 g of VOC.
For conventional nozzles:
  EPA’s AP‐42 (Chapter 5) estimates spillage at about 0.32 g/gallon dispensed
  ARB estimates 0.28 g/ gallon dispensed.*
    For EVR Stage II and conventional nozzles, ARB has nozzle standards to reduce spillage.**
  API estimates 0.14 g/gallon dispensed.***
Benzene mass in spilled fuel depends on benzene mass in liquid gasoline.
*ARB Revised Emission Factors for Gasoline Spillage at California Gasoline Dispensing Facilities, December 2013.
** See ARB CP201, CP207 and TPs 201‐.2C,.‐.2D, and ‐.2E.
***A Survey and Analysis of Liquid Gasoline Released to the Environment During Vehicle Refueling at Service Stations, API 4498, 1989.
10

## Slide 11: Technology for Refueling Emission Control
Stage II Vapor Recovery Technology: 70‐75% efficiency
ORVR Technology – 98% efficiency
11
Refueling vapors are blocked from escaping through the fill pipe and instead captured on the vehicle’s activated carbon
canister. The canister is purged during vehicle driving, and the
vapor is burned as fuel. ORVR technology is integrated with vehicle’s current evaporative control system hardware. ORVR designs also reduce spillage during refueling. ORVR is applicable to all types of
gasoline‐powered highway vehicles.
Refueling vapors are captured at the vehicle fillpipe outlet using a specially designed fuel nozzle and forced
into underground storage tank. In balance‐type systems, this returned vapor decreases fuel evaporation in the UST. During fuel delivery, if Stage I control is present, the tank vapors are routed back to the tanker truck as fuel is dropped. Stage II efficiency heavily dependent on user maintenance, inspections, and testing, as well as government oversight.

## Slide 12: Case Evaluations

## Slide 13: Case 1: The US (mature fuel and technology control programs)
0
100000
200000
300000
400000
500000
600000
700000
800000
Metric Tons VOC
2000 2002 2004 2006 2008 2010 2012 2014 2016 2018 2020 2022 2024 2026 2028 2030
Calendar Year
US VOC Refueling Emission Inventory
No Controls
With Vehicle‐based ORVR
With Pre‐existing Service Station Stage II & ORVR
0
1000
2000
3000
4000
5000
6000
7000
8000
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
2027
2028
2029
2030
Metric Tons Benzene
Calendar Year
US Benzene Refueling Emission Inventory
No Controls
With Vehicle‐based ORVR
With Pre‐existing Service Station Stage II & ORVR

## Slide 14: Case 2:China (benzene control and ORVR for 2020)
0
50000
100000
150000
200000
250000
Metric Tons VOC
Calendar Year
China VOC Refueling Emission Inventory
No Vehicle Controls
With Vehicle‐based ORVR
0
500
1000
1500
2000
2500
Metric Tons Benzene
Calendar Year
China Benzene Refueling Emission Inventory
No Vehicle Controls
With Vehicle‐based ORVR
China has Stage II in several major cities, but the implementation rate and efficiency are unknown.

## Slide 15: Case 3: EU 28 member states (widespread Stage II, but still phasing‐in )
15
0
300
600
900
1200
2010
2012
2014
2016
2018
2020
2022
2024
2026
2028
2030
2032
2034
2036
2038
2040
Metric Tons Benzene
No Stage II Control 1% Bz vol.
Inventory with 5% exemption
Certification Efficiency (85%)
Low End Efficiency Estimate (55%)
High End Efficiency Estimate (90%)
0
20000
40000
60000
80000
100000
2010
2012
2014
2016
2018
2020
2022
2024
2026
2028
2030
2032
2034
2036
2038
2040
Metric Tons VOC
Calendar Year Calendar Year
European Commission: Evaluation of Directive 1994/63/EC on VOC Emissions from Petrol Storage & Distribution and Directive 2009/126/EC on Petrol Vapor Recovery: Final Evaluation Report ‐ December, 2015.
EU Refueling VOC Emissions Inventory EU Refueling Benzene Emissions Inventory
160000 1800
140000
1500
120000
No Stage II Control
Inventory with 5% exemption
Certification Efficiency (85%)
Low End Efficiency Estimate (55%)
High End Efficiency Estimate (90%)

## Slide 16: Brazil (uses gasoline C blend (E25) and E100 fuel)
0
100
200
300
400
500
600
700
800
900
1000
2020
2021
2022
2023
2024
2025
2026
2027
2028
2029
2030
2031
2032
2033
2034
2035
2036
2037
2038
2039
2040
2041
2042
2043
2044
2045
2046
2047
2048
2049
Metric Tons Benzene
Calendar Year
Brazil Benzene Refueling Emission Inventory
Refueling Inventory with ORVR
Uncontrolled Refueling Inventory
Uncontrolled Refueling Inventory no E100
Refueling Inventory with ORVR no E100
0
10000
20000
30000
40000
50000
60000
70000
80000
90000
100000
2020
2021
2022
2023
2024
2025
2026
2027
2028
2029
2030
2031
2032
2033
2034
2035
2036
2037
2038
2039
2040
2041
2042
2043
2044
2045
2046
2047
2048
2049
Metric Tons VOC
Calendar Year
Brazil VOC Refueling Emission Inventory
VOC Refueling Inventory with ORVR
Uncontrolled VOC Refueling Inventory

## Slide 17: Six Areas Refueling Emission Inventory Trends
0
50000
100000
150000
200000
250000
2010 2012 2014 2016 2018 2020 2022 2024 2026 2028 2030 2032 2034 2036 2038 2040
Calendar Year
Metric Tons VOC
Vehicle Refueling VOC Emissions
US
Brazil
Brazil with ORVR
China Japan
EU
India
200
0
600
400
800
1000
1200
1400
1600
1800
2000
Metric Tons Benzene
Calendar Year
Vehicle Benzene Refueling Inventories
US
India Brazil
Japan China
EU
Brazil with ORVR

## Slide 18: Conclusions
Refueling emissions are significant sources of VOCs and air toxics
  Control provides reductions in ozone, SoA (PM2.5), and air toxics
  Inventories depend directly on gasoline and gasoline‐blend consumption
    Trends are definitely for reduced use of volatile fuels based on improved fuel economy requirements and powertrain electrification
There are well established control techniques available.
Vehicle control: 98% efficient
Stage II: 70‐75%
Fuel quality: RVP limits, benzene limits and use of oxygenate and gasoline‐ oxygenate blends
Analysis indicates significant inventory implications for Brazil and India which have no controls and project fuel large demand increase.
Significant implementation, cost, and cost‐effectiveness differences

## Slide 19
Thank you for your kind attention.
Glenn W. Passavant Ingevity Corporation
glenn.passavant@ingevity.com
517‐759‐9369

## Slide 20: EXTRA SLIDES

## Slide 21: Volatile Fuel Consumption
0
20
40
60
80
100
120
140
160
2000
2005
2010
2015
2025
2030
2035
2040
billion gallons/ year (gas+EtOH)
Brazil
US
2020
Calendar Year
China EU
Japan
India

## Slide 22: Vapor Generation During Refueling
A Study Of Variables that Effect The Amount of Vapor Emitted During the Refueling
of Automobiles, E.M. Liston, SRI, May 1975.
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
‐16
24
g VOC/Liter
1
∆T = Vehicle Tank Temp‐Dispensed Temp C◦
38 liters into 19 liters
57 liters into 19 liters
76 liters into 19 liters
19 liters into 19 liters
vapor/liquid volume ratio

## Slide 23: Benzene concentration in refueling vapor varies with fuel benzene content (mass % = 0.85 vol %)
HOWARD E. RUNION (1975) Benzene in Gasoline, American Industrial Hygiene Association Journal, 36:5, 338‐350
vol% Bz vapor = 0.43*(vol % Bz liquid)
23

## Slide 24: Vehicle Benzene Refueling Inventories
2000
1800
1600
1400
1200
1000
800
600
400
200
0
2020
2021
2022
2023
2024 2025 2026
2027
2028
2029 2030
2031
2032
2033
2034
2035 2036
2037
2038
2039
2040
Metric Tons
Calendar Year
US
Japan
EU
India
China
Brazil with ORVR
Brazil

## Slide 25: Time‐series Comparison of Refueling VOC Emission Inventories – 6 areas
50000
100000
150000
200000
250000
Metric Tons VOC
0
2010 2011 2012 2013 2014 2015 2016 2017 2018 2019 2020 2021 2022 2023 2024 2025 2026 2027 2028 2029 2030 2031 2032 2033 2034 2035 2036 2037 2038 2039 2040
Calendar Year
US China EU Brazil Japan India

## Slide 26: Benzene refueling emission rate is impacted by dispensed (Td) and fuel tank temperature (Tt)
Benzene Refueling Emissions: % vol vs. Td ;∆T= 0
Benzene Refueling Emissions: % vol vs.
∆T where ∆T=(Tt‐Td); Td =70F
0
0.01
0.02
0.03
0.04
0.05
0.06
0.07
0.08
g Bz/gallon dispensed
0.5% 1% 1.5% 2% 2.5%
‐30
‐20
‐10 0
10
20
30
0
0.01
0.02
0.03
0.04
0.05
0.06
0.07
g Bz/gallon dispensed
0.5% 1% 1.5% 2% 2.5%
50
55
60
65
70
75
80
Bz (g/gal) = 0.038*(% Bzm)‐(1.60 E‐4 *Td)‐(4.24 E‐4*∆T): Equation from: SAE Paper 861559: Factors Influencing Benzene Emissions from Passenger Cart Refueling, October 1986.
26