## Slide 1: DAY 2 - Short Course on Introduction to Air Pollution Modeling Online Program All times UK BST https://www.wessex.ac.uk/courses/short-course-on-introduction-to-air-pollution-modelling © Paolo Zannetti & Wessex Institute of Technology
Lecturer: Dr. Paolo Zannetti, QEP
zannetti@envirocomp.org
President, The EnviroComp Institute
  www.envirocomp.org
EnviroComp Consulting, Inc.
www.envirocomp.com
Director, Air Pollution Scientific Initiative (APSI)
www.apsi.tech

## Slide 2: DAY 2 - Wednesday 12 May 2021
Time | Session | Topics
1300-1350 | Mathematical/Numerical Modeling of Air Pollution Phenomena (Part I) | Emission Estimates US EPA AP-42 The Gaussian Model Grid Models
1400-1450 | Mathematical/Numerical Modeling of Air Pollution Phenomena (Part II) | Modeling of Chemical/Photochemical Reactions Dry/Wet Deposition Modeling Regulatory Modeling Particle Modeling (Monte Carlo)
1500-1550 | Mathematical/Numerical Effects on Human Health Modeling of Air Pollution Other Adverse Effects Adverse Effects | 
1630-1830 | 1-to-1 ad-hoc support | 

## Slide 3: Lesson 1A Mathematical/Numerical Modeling of Air Pollution Phenomena (Part I) 2-Intro to APM.pptx

## Slide 4: Introduction
Dispersion Modeling:
  Emissions  Concentrations
Emissions  mass/time
  e.g., grams/second (g/s)
Emissions cause ambient concentrations  mass/volume
  E.g., micrograms/cubic meter (µg/m3)
  Gasses are measured in parts per millions (ppm) or parts per billions (ppb)
    Conversion: https://paceport.pacelabs.com/ClientPortal/conversiontool.jsp

## Slide 5: Lesson 1B Mathematical/Numerical Modeling of Air Pollution Phenomena (Part I) Emission Estimates

## Slide 6: Emission Estimates
In most case you will need an emission expert/industrial engineer
  Mass balance calculations
  Other methods
E.g., Methane Emissions from the Aliso Canyon Natural Gas Leak Incident
https://ww2.arb.ca.gov/sites/default/files/2020-07/aliso_canyon_methane_emissions-arb_final.pdf
Flaring episode 

## Slide 7
Flaring episode

## Slide 9: Lesson 1C Mathematical/Numerical Modeling of Air Pollution Phenomena (Part I) Emission Estimates US EPA AP-42

## Slide 10: US EPA AP-42
https://www.epa.gov/air-emissions-factors-and-quantification/ap-42-compilation-air-emissions-factors

## Slide 11: Lesson 1D Mathematical/Numerical Modeling of Air Pollution Phenomena (Part I) The Gaussian Model

## Slide 12
30

## Slide 13: Gaussian Distribution

## Slide 14: Gaussian Plume Model

## Slide 16: Gaussian Plume Model – Emission rate Q in (0,0,H) In the point (x,y,z) the concentration c is:
Sigma y and sigma z (slides 32 and 33):
  https://ansn.iaea.org/Common/Topics/OpenTopic.aspx?ID=13012 
Free calculator: http://www.csun.edu/~vchsc006/469/gauss1.html
Free SCREEN model: get it today and start playing!!
  https://www.weblakes.com/products/screen/index.html
Sigma y and sigma z (slides 32 and 33):
  https://ansn.iaea.org/Common/Topics/OpenTopic.aspx?ID=13012 
Free calculator: http://www.csun.edu/~vchsc006/469/gauss1.html
Free SCREEN model: get it today and start playing!!
  https://www.weblakes.com/products/screen/index.html

## Slide 17: Dispersion Coefficients: Horizontal
17

## Slide 18: Dispersion Coefficients: Vertical
18

## Slide 19: Gaussian Plume Chapter
https://www.envirocomp.com/airpollution/Ch.7.PDF

## Slide 20: Plume Rise
H = h + ∆h
  H final height
  h stack height
  ∆h plume rise
Basic plume rise formula: next
Full chapter:
  https://www.apsi.tech/modeling_plumerise_advanced.html

## Slide 21: Plume Rise
For neutral and unstable atmospheric conditions, buoyant rise can be calculated by
(F  55 m4 / s3 )
21.425F 0.75
u
38.71F 0.6
plumerise
h 
(F  55 m4 / s3 )
21
u
hplume rise 

F  gV d 2 (T T ) / 4T
s s a S
where buoyancy flux is
Vs: Stack exit velocity, m/s
d: top inside stack diameter, m Ts: stack gas temperature, K Ta: ambient temperature, K
g: gravity, 9.8 m/s2
Buoyant plume: Initial buoyancy >> initial momentum
Forced plume: Jet:
Initial buoyancy ~ initial momentum Initial buoyancy << initial momentum

## Slide 22: Most used Gaussian Plume Model: AERMOD
US EPA preferred model (<50 km)
Static: every hour is a steady-state
Well-tested
Used all over the world
Free software from US EPA
  https://www.epa.gov/scram/air-quality-dispersion-modeling-preferred-and-recommended-models#aermod
User-friendly versions can be purchased, e.g.:
  https://www.weblakes.com/products/aermod/index.html

## Slide 23: Main US EPA Pre-processors for AERMOD
AERSURFACE - https://www.epa.gov/scram/air-quality-dispersion-modeling-related-model-support-programs#aersurface
  A tool that processes land cover data to determine the surface characteristics for use in AERMET
AERMET - https://www.epa.gov/scram/meteorological-processors-and-accessory-programs#aermet
  A meteorological data preprocessor for AERMOD
AERMAP - https://www.epa.gov/scram/air-quality-dispersion-modeling-related-model-support-programs#aermap
  It processes commercially available Digital Elevation Data and creates a file suitable for use within an AERMOD control file
My suggestion: * use user-friendly versions of AERMOD, e.g.:
https://www.weblakes.com/products/aermod/index.html
  * use AERMOD-ready meteorological data, e.g.:
  https://www.weblakes.com/services/met_order.html
  https://www.enviroware.com/portfolio/meteodata/

## Slide 24: Gaussian Puff Models
Dynamic
3D
Work with calm/low winds

## Slide 25: Most used Gaussian Puff Model: CALPUFF
Accepted by US EPA (especially > 50 km)
Well tested
Used all over the world
More complex to use than AERMOD
Better physical representation
Free software: http://www.src.com/
User-friendly version can be purchased, e.g.:
  https://www.weblakes.com/products/calpuff/index.html

## Slide 26: Lesson 1E Mathematical/Numerical Modeling of Air Pollution Phenomena (Part I) Grid Models

## Slide 27: Grid Models in Atmospheric Sciences Global Scale

## Slide 28: Grid Models in Atmospheric Sciences Continental Scale

## Slide 29: Grid Models in Atmospheric Sciences Regional Scale

## Slide 30: Grid Models
Used today:
  Meteorological modeling
  Advanced plume simulations (Computations Fluid Dynamics , CFD)
    e.g.: https://www.witpress.com/elibrary/sdp-volumes/11/4/1330
    Plume rise
    Street canyon
    Indoor modeling
  Photochemical modeling ( next lesson)

## Slide 32: Lesson 2A Mathematical/Numerical Modeling of Air Pollution Phenomena (Part II)

## Slide 33: Questions on Lesson 1 ??

## Slide 34: Lesson 2B Mathematical/Numerical Modeling of Air Pollution Phenomena (Part II) Modeling of Chemical/Photochemical Reactions

## Slide 35: Photochemical Smog  Ozone
METR113_Spring2020_Lecture8.pptx

## Slide 36
Empirical kinetic modeling approach (EKMA) diagram. SOURCE:
NRC 1991, adapted from Dodge 1977.
Challenge: Non-Linearity (e.g. Ozone)

## Slide 37: Photochemical Models
https://www.epa.gov/scram/photochemical-air-quality-modeling
  https://www.epa.gov/cmaq
  https://www.camx.com/
  http://remsad.icfconsulting.com/
  http://uamv.icfconsulting.com/
I recommend CAMx (all free)
Difficult to use, but no alternative…

## Slide 38: Lesson 2C Mathematical/Numerical Modeling of Air Pollution Phenomena (Part II) Dry/Wet Deposition Modeling

## Slide 39: Deposition
The way the atmosphere cleans itself  soil, water pollution
All models have dry/wet deposition formulations
Simple formulas: simple decrease of plume/puff concentration
  E.g., 1% per hour
Complex formulations
  Chapter11-TransferofPollutantsbetweentheAtmosphereandSurfaces.ppt
  https://www.apsi.tech/modeling_depositionphenomema_advanced.html

## Slide 40: Lesson 2D Mathematical/Numerical Modeling of Air Pollution Phenomena (Part II) Regulatory Modeling

## Slide 41: Regulatory Management
(3-Air Quality Management - US.pptx)
(4-Air Quality Management in Europe.pptx)

## Slide 42: Lesson 2E Mathematical/Numerical Modeling of Air Pollution Phenomena (Part II) Particle Modeling – Monte Carlo

## Slide 43: Particle Modeling (PM) – Monte Carlo (MC)
PM simulate air pollution by a series of fictitious moving points or “particles”
Example: plume animation plume animation2
Advanced method – not frequently used – very powerful
  Both short-range (animations)
  Long range: https://cfpl.ae.utexas.edu/modeling-volcanic-plumes-on-jupiters-moon-io
Free model (LAPMOD):
  https://www.enviroware.com/lapmod/

## Slide 45: Lesson 3A Mathematical/Numerical Modeling of Air Pollution Adverse Effects

## Slide 46: Adverse Effects of Air Pollution
Human health
Animals & Plants
Visibility (e.g., in national parks)
Materials (e.g., corrosion)
Agricultural production
Property values
Etc. ALL THESE EFFECTS CAN BE MODELED (to a certain extent…)

## Slide 47: Lesson 3B Mathematical/Numerical Modeling of Air Pollution Adverse Effects Effects on Human Health

## Slide 48: For example: Chronic/Long-Term Health Risk Assessment
DOSE:
Given knowledge of …
Concentration (C) = mass pollutant per volume air
Inhalation Rate (I) = volume of air breathed per time
Time duration of exposure (t)
Multiply the three …
C × I × t = D
Dose is calculated over a “lifetime” (70 years is standard time)
Need knowledge of concentrations over this time
Need this at all places of exposure
  Workplace
  Indoor (e.g., residence)
  Outdoor ambient air
where ‘D’ is dose
(mass of pollution inhaled)

## Slide 49: Dose - Response Relationships
probability
Lower threshold below which
“no response”. Called “reference
concentration” (RfC) by CARB
No lower threshold,
i.e. any non-zero dose
increases probability
http://www.epa.gov/ttn/atw/3_90_024.html

## Slide 50: Human Health
HARP software - https://ww2.arb.ca.gov/our-work/programs/hot-spots-analysis-reporting-program/about
  HARP is divided into three programs: the Emissions Inventory Module (EIM), Air Dispersion Modeling and Risk Tool (ADMRT), and Risk Assessment Standalone Tool (RAST).
User Guide: https://ww2.arb.ca.gov/sites/default/files/classic//toxics/harp/docs2/harp2rastuserguide.pdf
Calculates cancer and noncancer (acute, 8-hour, and chronic) health impacts using the new risk assessment guidelines in the OEHHA Guidance Manual (OEHHA, 2015) - https://oehha.ca.gov/media/downloads/crnr/2015guidancemanual.pdf
(health-risk-slides.pptx)

## Slide 51: Lesson 3C Mathematical/Numerical Modeling of Air Pollution Adverse Effects Other Adverse Effects

## Slide 52: Other Adverse Effects
Animals
  E.g.: https://www.canada.ca/en/environment-climate-change/services/air-pollution/quality-environment-economy/ecosystem/wild-animals.html
Plants
  E.g.: https://link.springer.com/book/10.1007/978-981-10-1201-3
Visibility (e.g., in national parks)  visibility modeling
  https://www.epa.gov/visibility

## Slide 54: Cont.
Materials (e.g., corrosion)
  E.g.: Pollution Damage to Works of Art https://link.springer.com/chapter/10.1007%2F978-3-0348-5779-6_7
Agricultural production; e.g. http://www.omafra.gov.on.ca/english/crops/facts/01-015.htm
Property values, e.g. https://www.ncbi.nlm.nih.gov/pmc/articles/PMC6025591/

## Slide 56: Lesson 4 1-to-1 ad-hoc support