## Slide 1
Transfer of Pollutants
between the Atmosphere and Surfaces
Dry deposition
Wet deposition
Reemissions and natural emissions
  General considerations
  Reemissions of particles by on-road traffic
  Wind-blown dust
  Sea-salt emissions

## Slide 2: Atmospheric Dry Deposition
Atmospheric dry deposition is defined as the transfer of mass from the atmosphere to surfaces by processes other than wet precipitation. It involves various processes:
  Sedimentation
  Diffusion toward a surface
  Adsorption on a surface
  Absorption (including dissolution) into a liquid film
  Chemical reaction on a surface

## Slide 3: Transfer from the Atmosphere to Surfaces
The two fundamental processes are
  Gravity: sedimentation of particles (dominant for coarse particles)
  Various diffusion processes: combination of turbulent diffusion followed by molecular diffusion (for gases), brownian diffusion (for particles, dominant for ultrafine particles), and impacts by inertia and/or interception (for particles, dominant for fine particles)

## Slide 4: Sedimentation
The acceleration of a moving particle in the atmosphere is governed by two forces, which are gravity and the resistance of the air (friction).
gravity force of friction (Stokes)
Archimedes
mp >> mair ; therefore, the buoyancy force of Archimedes may be neglected
When the friction of the particle against the air becomes commensurate with gravity, one obtains the fall velocity of the particle from the following equation:

## Slide 5: Sedimentation
For Re << 1 (particles), the particle sedimentation velocity is given by:
where p is the particle density,  v,a is the dynamic viscosity of the air, dp is the diameter of the particle, and cc is the Cunningham correction factor, which is a function of the particle size.
For fine particles, the sedimentation velocity decreases as the diameter decreases (proportional to the square of the diameter) and, therefore, becomes negligible for fine and ultrafine particles.

## Slide 6: Sedimentation
For Re >> 1 (raindrops; formula of Kessler, 1995 ; dgp is in m and vsf in m/s):
For large coarse particles and raindrops, the terminal fall velocity increases with the diameter, but not proportionally because of the drag coefficient (cD), which is a function of the particle/drop diameter. For raindrops, the fall velocity is approximately proportional to the square-root of the diameter.

## Slide 7: Dry Deposition
Dry deposition by diffusion processes is mostly function of the following characteristics:
  Atmospheric turbulence: it determines the atmospheric flux that transfers the pollutant toward the surface.
  The pollutant properties: solubility and chemical reactivity for gases; size, density, and shape for particles
  The characteristics of the surface: wetness, roughness, reactivity, surface area, etc.

## Slide 8: Diffusion
Turbulent diffusion: it brings the pollutant in proximity of the surface.
Diffusion in a laminar regime (i.e., near the surface, ~ a few mm):
  Gases: molecular diffusion
  Fine particles: brownian diffusion, impact by interception and/or inertia

## Slide 9: Deposition on the Surface
Particles: One typically assumes that the particles remains on the surface after contact, but a bouncing coefficient may be used.
Gases: The gas molecule deposits by adsorption, absorption (for example, dissolution in a liquid) or chemical reaction on the surface

## Slide 10: Dry Deposition Processes
(1) Vertical turbulent transfer in the atmosphere
(2) Transfer by diffusion (molecular for gases, brownian for particles) in a very thin (a few millimeters) quasi-laminar layer above the surface
(3) Deposition by interception or inertia (for particles), adsorption, absorption or reaction (for gases)
Surface
1
2
3

## Slide 11: Resistance Approach
This approach for dry deposition by diffusion processes is based on an analogy with electrical resistances in series.
Each stage is represented by a resistance to the deposition process.
Resistances are expressed in units of s/cm and the inverse of the total resistance is the dry deposition velocity.
Aerodynamic resistance
Diffusion resistance
Surface resistance
3
2
1
Atmospheric surface layer
Quasi-laminar layer
Surface

## Slide 12: Resistance Approach
Gaseous pollutants: 1 / vd = rt = ra + rb + rc
Fine particles: 1 / vd = rt = ra + rb
In this latter case, the sedimentation velocity is neglected and the surface resistance is considered to be zero (interception, inertia, and brownian diffusion are treated jointly in the diffusion resistance rb)
The dry deposition flux, Fd (g m-2 s-1), is defined as the product of a dry deposition velocity, vd (m s-1), and the pollutant concentration, C (g m-3)
Fd = vd C

## Slide 13: Dry Deposition of Fine Particles
Impact by inertia: proportional to the mass of the particle, therefore, proportional to the volume (dp3) and particle density
Impact by interception: proportional to the cross-sectional surface area of the particle, i.e., dp2

## Slide 14: Sedimentation + Deposition by Diffusion
For a large coarse particle: vs >> 1/rt => vd = vs
For a fine particle: vs << 1/rt => vd = 1/rt
Particles with a non-negligible sedimentation velocity (Venkatram and Pleim, 1999):
Fd = K dC/dz + vs C
diffusion sedimentaton

## Slide 15: Dry Deposition of Particles
The dry deposition velocities of particles depend on
(1) meteorological conditions and surface characteristics and
(2) particle size.
Fine particles (i.e., those with a diameter between 0.1 and 1 m have the lowest dry deposition velocities.
The sedimentation velocity is important only for large coarse particles.

## Slide 16: Reduction of Particulate Emissions by Filtration
Particle filters (e.g., baghouses, diesel particle filters) collect particles using the same processes as those involved in atmospheric processes: impact by inertia and interception, brownian diffusion.
In electrostatic precipitators (ESP), electrostatic forces play the major role.

## Slide 17: Inhalation of Particles Influence of Particle Size
The same deposition processes as those taking place in the atmosphere occur in the respiratory tract: therefore, particles with a diameter between 0.1 and 1 m penetrate the deepest into the lungs.
However, ultrafine particles (those with a diameter less than 0.1 m) have a greater probability to deposit within the lungs than fine particles (i.e., those with a diameter greater than 0.1 m).

## Slide 18: Dry Deposition Mass Balance within the Planetary Boundary Layer
Dry deposition flux:
Fd = vd C
Change with time of the concentration within the boundary layer:
dC/dt = - vd C / hPBL
C = C0 exp( - (vd / hPBL) t)
hPBL
vd
Planetary Boundary Layer (PBL)

## Slide 19: Atmospheric Wet Deposition
Wet deposition may be defined as the transfer of mass from the atmosphere to surfaces via precipitation:
  Rain
  Snow
  Hail
  Fog settling
  Mountain cloud impact

## Slide 20: Pollutant Scavenging
The two fundamental processes are:
  The scavenging of gaseous and particulate pollutants within the cloud: rainout
  The scavenging of gaseous and particulate pollutants by raindrops below the cloud base: washout

## Slide 21: Wet Deposition Flux Scavenging of Pollutants below the Cloud
The change with time of the concentration of an atmospheric pollutant (gas or particle) due to precipitation scavenging is as follows:
C(t) = C0 exp(-  t)
where C0 is the pollutant concentration at the beginning of the precipitation event.
The wet deposition flux is given by the following expression:
Fw(t) = C(t)  hc
where hc is the height of the cloud base above ground level (i.e., the height of the air column scavenged by precipitation).

## Slide 22: Scavenging Coefficient of Gaseous Pollutants
The scavenging coeffiient depends on precipitation intensity:
 = (6 km Ip) / (dr vs,r)
Ip: precipitation intensity; (/6) dr3 vs,rf Nrp
dr: raindrop diameter
Vs,r: fall velocity of raindrops
Ngp: number of raindrops per unit volume of air for that precipitation event
km: mas transfer coefficient of the gaseous pollutant in the air
However, precipitation intensity depends on raindrop size and the mass transfer coefficient also depends on raindrop size. Therefore, the scavenging coefficient is less than proportional to precipitation intensity.

## Slide 23: Wet Deposition Flux Scavenging Coefficient of Nitric Acid
Precipitation intensity | 1 mm/h | 5 mm/h | 10 mm/h | 20 mm/h
HNO3 | 5 x 10-5 s-1 | 1.5 x 10-4 s-1 | 2 x 10-4 s-1 | 3.5 x 10-4 s-1
Particule fine (2,5 m) | 3 x 10-7 s-1 | 8 x 10-7 s-1 | 1 x 10-6 s-1 | 2 x 10-6 s-1

## Slide 24: Wet Deposition of Particles
Scavenging of fine particles occurs via various processes:
Within the cloud:
- formation of cloud droplets from atmospheric particles (Aïtken nucleation particles and fine particles)
- collision of particles with cloud droplets
Below the cloud:
- scavenging by collision of particles with raindrops

## Slide 25
The scavenging coefficient is as follows:
 = (/2) Ip E(dr, dp) / dr
Ip: precipitation intensity ; (/6) dr3 vs,rf Nrp
dr: raindrop diameter
dp: particle diameter
Vs,r: fall velocity of the raindrop
E(dr, dp): collision efficiency of particles and raindrops (<1)
Nrp: number of raindrops per unit volume of air for that precipitation event
However, precipitation intensity depends on raindrop size and the collision efficiency depends also on raindrop size. Therefore, the scavenging coefficient is less than proportional to precipitation intensity.
Scavenging Coefficient of Particles

## Slide 26
Collision efficiency of raindrops and particles
Scavenging Coefficient of Particles
Brownian diffusion dominates for ultrafine particles, i.e. those particles of diameter < 0.1 m.
Interception becomes important for fine particles with diameter in the range of 0.1 to 2.5 m and coarse particles up to 5 m diameter.
Inertia dominates for coarse particles with diameter > 5 m.
The collision efficiency tends toward 1 for particles of diameter > 10 m.

## Slide 27
Example of scavenging coefficients for particles (precipitation intensity between 1. 5 and 25 mm/h)
Scavenging Coefficient of Particles

## Slide 28: Scavenging Coefficients
Precipitation intensity | 1 mm/h | 5 mm/h | 10 mm/h | 20 mm/h
HNO3 | 5 x 10-5 s-1 | 1.5 x 10-4 s-1 | 2 x 10-4 s-1 | 3.5 x 10-4 s-1
Fine particles (diameter = 2.5 m) | 3 x 10-7 s-1 | 8 x 10-7 s-1 | 1 x 10-6 s-1 | 2 x 10-6 s-1

## Slide 29: Dry and Wet Deposition
Wet deposition occurs intermittently (mostly when it rains); it rains only 2 to 5 % of the time in the mid-latitudes.
Dry deposition occurs all the time; however, the dry deposition flux is typically smaller (per unit time) than the wet deposition flux when it rains.
Wet deposition affects the entire atmospheric column below cloud base.
Dry deposition affects mostly the pollutants located near the surface (typically within the mixing layer) and it is more efficient in areas with complex surfaces (e.g., vegetation, built areas).

## Slide 30: Reemissions and Natural Emissions
Reemissions
  Grasshopper effect
  Resuspension of particles by on-road traffic
Wind-driven natural emissions
  Wind-blown dust
  Sea-salt emissions

## Slide 31: Grasshopper Effect
Semi-volatile pollutants such as persistent organic pollutants (POP) have a volatility that varies with temperature. They will deposit more readily when the temperature is low as they are mostly present in the particulate phase. When the ambient temperature increases, their gas/particle partitioning will tend to shift toward the gas phase and they will be reemitted as gases.
A succession of deposition and reemission steps of a semi-volatile pollutant is called the “grasshopper effect”, because the pollutant may be transported over long distances (several thousands of kilometers) via a series of deposition/reemission “hops”.
The reemission of a pollutant may also occur following a chemical transformation; e.g., N2O from soils and Hg0 from soils and water bodies.

## Slide 32: Resuspension of Particles by On-road Traffic
Vehicles leads to resuspension of particles present on the roadway.
One assumes that the majority of this particulate mass deposited on the roadway consists of coarse particles resulting from wear of brake-pads, tires, and road surface.
The NORTRIP model (Denbigh et al., 2013) uses a mass balance based on deposition of particles on the roadway and resuspension of particles by traffic:
Ml,r: Mass of particles on the roadway per unit length
Fl,r: Deposition rate particles onto the roadway per unit length
Sl,r: Resuspension rate of particles from the roadway per unit length
and runoff of particles during rain events

## Slide 33: Resuspension of Particles by On-road Traffic
The resuspension rate of particles from the roadway, Sl,r, is proportional to the particulate mass present on the roadway, Ml,r, the number and type of vehicles (trucks, passenger cars) travelling on the roadway, and the fraction of particles resuspended per vehicle (a function of vehicle type, vehicle speed, and moisture on the road).
Nv: Number of vehicles of type v travelling per unit time
fv: Fraction of particles resuspended per vehicle
vv: Vehicle speed

## Slide 34: Resuspension of Particles by On-road Traffic
Comparison of direct particle emissions from vehicles
and particle resuspension by traffic
Urban freeway
vv = 69 km h-1
dry conditions
Suburban boulevard
vv = 32 km h-1
wet conditions
Source: adapted from Thouron, 2017

## Slide 35: Wind-blown Dust
Resuspension of particles from an erodible surface by wind erosion (aeolian resuspension) may contribute significantly to atmospheric particle concentrations and these particles may be transported over long distances.
The aeolian resuspension process consists first in a hydrodynamic lifting of particles available at the surface. These particles may subsequently deposit back to the surface, especially if they are large particles. This saltation leads to impacts of particles on the surface and generates smaller particles, which become available for resuspension.

## Slide 36: Wind-blown Dust
The vertical flux of particles resuspended by wind erosion, Fe, may be calculated according the expression developed by Kok et al. (2011), based on a literature review of theory and experimental data.
An upper limit of the resuspension vertical flux may be estimated for fine particles as follows:
fer: erodible fraction of the soil
fclay: clay fraction of the soil
a: density of the air
u*: friction velocity
u*t: threshold friction velocity for soil erosion
u*st: threshold friction velocity at standard conditions

## Slide 37: Sea-salt Emissions
Sea and ocean waves lead to the formation of sea salt droplets in suspension in the air. The evaporation of those droplets may lead to the formation of sea salt aerosol particles. Wave formation depends strongly on wind speed.
Different processes are involved in the formation of sea salt droplets. Fine particles (dp < 1 mm) result from he bursting of bubbles. Other processes lead to the formation of larger particles that settled back rapidly to the sea surface.
Sea salt particle formation may be important and may affect PM concentrations in coastal areas.

## Slide 38: Sea-salt Emissions
Monahan et al. (1986) have developed one of the first algorithms that have been widely used to simulate sea salt particle formation. The emission flux may be written as the density function of the particle vertical flux emitted from the sea surface, Fs, as a function of particle diameter.
u10: wind speed at 10 m
dp: sea-salt particle diameter
Tss: sea surface temperature
ss: salinity