## Slide 1: 6 - Air Quality Modeling and Software
US Environmental Protection Agency (EPA)

## Slide 2: Best Resource: SCRAM
http://www.epa.gov/scram001/
This website is maintained by EPA's Air Quality Modeling Group (AQMG).
Sections:
  Air Quality Models
  Modeling Applications and Tools
  Modeling Guidance & Support
  Meteorological Data & Processors
  Conferences & Workshops
  Reports & Journal Articles

## Slide 3: Air Quality Models
Air quality models use mathematical and numerical techniques to simulate the physical and chemical processes that affect air pollutants as they disperse and react in the atmosphere. Based on inputs of meteorological data and source information like emission rates and stack height, these models are designed to characterize primary pollutants that are emitted directly into the atmosphere and, in some cases, secondary pollutants that are formed as a result of complex chemical reactions within the atmosphere.
These models are important to our air quality management system because they are widely used by agencies tasked with controlling air pollution to both identify source contributions to air quality problems and assist in the design of effective strategies to reduce harmful air pollutants.

## Slide 4: Cont.
For example, air quality models can be used during the permitting process to verify that a new source will not exceed ambient air quality standards or, if necessary, determine appropriate additional control requirements.
In addition, air quality models can also be used to predict future pollutant concentrations from multiple sources after the implementation of a new regulatory program, in order to estimate the effectiveness of the program in reducing harmful exposures to humans and the environment.

## Slide 5: Most common AQ models
Dispersion Modeling - These models are typically used in the permitting process to estimate the concentration of pollutants at specified ground-level receptors surrounding an emissions source.
Photochemical Modeling - These models are typically used in regulatory or policy assessments to simulate the impacts from all sources by estimating pollutant concentrations and deposition of both inert and chemically reactive pollutants over large spatial scales.
Receptor Modeling - These models are observational techniques which use the chemical and physical characteristics of gases and particles measured at source and receptor to both identify the presence of and to quantify source contributions to receptor concentrations.

## Slide 6: Dispersion Modeling
Dispersion modeling uses mathematical formulations to characterize the atmospheric processes that disperse a pollutant emitted by a source.
These air quality models are used to determine
  compliance with National Ambient Air Quality Standards (NAAQS), and other regulatory requirements such as
  New Source Review (NSR) and
  Prevention of Significant Deterioration (PSD) regulations.

## Slide 7: Preferred/Recommended Models
AERMOD Modeling System - A steady-state plume model that incorporates air dispersion based on planetary boundary layer turbulence structure and scaling concepts, including treatment of both surface and elevated sources, and both simple and complex terrain.
CALPUFF Modeling System - A non-steady-state puff dispersion model that simulates the effects of time- and space-varying meteorological conditions on pollution transport, transformation, and removal. CALPUFF can be applied for long-range transport, complex terrain, and calm conditions.
Other Models - Other dispersion models including BLP, CALINE3, CAL3QHC/CAL3QHCR, CTDMPLUS, and OCD.

## Slide 8: AERMOD Modeling System
The American Meteorological Society/Environmental Protection Agency Regulatory Model Improvement Committee (AERMIC) was formed to introduce state-of-the-art modeling concepts into the EPA's air quality models.
Through AERMIC, a modeling system, AERMOD, was introduced that incorporated air dispersion based on planetary boundary layer turbulence structure and scaling concepts, including treatment of both surface and elevated sources, and both simple and complex terrain.
There are two input data processors that are regulatory components of the AERMOD modeling system:
  AERMET, a meteorological data preprocessor that incorporates air dispersion based on planetary boundary layer turbulence structure and scaling concepts, and
  AERMAP, a terrain data preprocessor that incorporates complex terrain using USGS Digital Elevation Data.
Other non-regulatory components of this system include: AERSCREEN, a screening version of AERMOD; AERSURFACE, a surface characteristics preprocessor, and BPIPPRIME, a multi-building dimensions program incorporating the GEP technical procedures for PRIME applications.

## Slide 9: CALPUFF Modeling System
CALPUFF is a multi-layer, multi-species non-steady-state puff dispersion model that simulates the effects of time- and space-varying meteorological conditions on pollution transport, transformation and removal.
CALPUFF can be applied on scales of tens to hundreds of kilometers. It includes algorithms for subgrid scale effects (such as terrain impingement), as well as, longer range effects (such as pollutant removal due to wet scavenging and dry deposition, chemical transformation, and visibility effects of particulate matter concentrations).

## Slide 10: Cont. (http://www.src.com/calpuff/calpuff1.htm)
CALPUFF is an advanced non-steady-state meteorological and air quality modeling system developed by ASG scientists. It is maintained by the model developers and distributed by TRC.
The model has been adopted by the U.S. Environmental Protection Agency (U.S. EPA) in its Guideline on Air Quality Models as the preferred model for assessing long range transport of pollutants and their impacts on Federal Class I areas and on a case-by-case basis for certain near-field applications involving complex meteorological conditions.
The modeling system consists of three main components and a set of preprocessing and postprocessing programs. The main components of the modeling system are
  CALMET (a diagnostic 3-dimensional meteorological model),
  CALPUFF (an air quality dispersion model), and
  CALPOST (a postprocessing package).
Each of these programs has a graphical user interface (GUI).
In addition to these components, there are numerous other processors that may be used to prepare
  geophysical (land use and terrain) data in many standard formats,
  meteorological data (surface, upper air, precipitation, and buoy data), and
  interfaces to other models such as the Penn State/NCAR Mesoscale Model (MM5), the National Centers for Environmental Prediction (NCEP) Eta/NAM and RUC models, the Weather Research and Forecasting (WRF) model and the RAMS model.

## Slide 11: Other Preferred/Recommended Dispersion Models
CAL3QHC/CAL3QHCR CAL3QHC is a CALINE3 based CO model with queuing and hot spot calculations and with a traffic model to calculate delays and queues that occur at signalized intersections; CAL3QHCR is a more refined version based on CAL3QHC that requires local meteorological data.
OCD Offshore and Coastal Dispersion Model Version 5 (OCD) is a straight line Gaussian model developed to determine the impact of offshore emissions from point, area or line sources on the air quality of coastal regions. OCD incorporates overwater plume transport and dispersion as well as changes that occur as the plume crosses the shoreline. Hourly meteorological data are needed from both offshore and onshore locations.

## Slide 12: Alternative Models
These models can be used in regulatory applications with case-by-case justification to the Reviewing Authority, e.g.:
  DEGADIS DEGADIS simulates the atmospheric dispersion at ground-level of area source dense gas (or aerosol) clouds released with zero momentum into the atmospheric boundary layer over flat, level terrain. The model describes the dispersion processes which accompany the ensuing gravity-driven flow and entrainment of the gas into the boundary layer.
  ISC3 ISC3 is a steady-state Gaussian plume model which can be used to assess pollutant concentrations from a wide variety of sources associated with an industrial complex. This model can account for the following: settling and dry deposition of particles; downwash; point, area, line, and volume sources; plume rise as a function of downwind distance; separation of point sources; and limited terrain adjustment. ISC3 operates in both long-term and short-term modes.

## Slide 13: Cont.
PLUVUEII A model used for estimating visual range reduction and atmospheric discoloration caused by plumes resulting from the emissions of particles, nitrogen oxides, and sulfur oxides from a single source. The model predicts the transport, dispersion, chemical reactions, optical effects and surface deposition of point or area source emissions.
SCIPUFF Second-order Closure Integrated PUFF Model (SCIPUFF) is a Lagrangian puff dispersion model that uses a collection of Gaussian puffs to predict three-dimensional, time-dependent pollutant concentrations. In addition to the average concentration value, SCIPUFF provides a prediction of the statistical variance in the concentration field resulting from the random fluctuations in the wind field.

## Slide 14: Photochemical Modeling
Photochemical air quality models have become widely recognized and routinely utilized tools for regulatory analysis and attainment demonstrations by assessing the effectiveness of control strategies.
These photochemical models are large-scale air quality models that simulate the changes of pollutant concentrations in the atmosphere using a set of mathematical equations characterizing the chemical and physical processes in the atmosphere.
These models are applied at multiple spatial scales from local, regional, national, and global.
There are two types of photochemical air quality models commonly used in air quality assessments:
  the Lagrangian trajectory model that employs a moving frame of reference, and
  the Eulerian grid model that uses a fixed coordinate system with respect to the ground.
Most of the current operational photochemical air quality models have adopted the three-dimensional Eulerian grid modeling mainly because of its ability to better and more fully characterize physical processes in the atmosphere and predict the species concentrations throughout the entire model domain.

## Slide 15: Available photochemical air quality models
Community Multi-scale Air Quality (CMAQ) - EPA's CMAQ modeling system is supported by the Community Modeling and Analysis System (CMAS) Center. The CMAQ model includes state-of-the-science capabilities for conducting urban to regional scale simulations of multiple air quality issues, including tropospheric ozone, fine particles, toxics, acid deposition, and visibility degradation.
Comprehensive Air quality Model with extensions (CAMx) - The CAMx model simulates air quality over many geographic scales. The model treats a wide variety of inert and chemically active pollutants, including ozone, particulate matter, inorganic and organic PM2.5/PM10, and mercury and other toxics. CAMx also has plume-in-grid and source apportionment capabilities.
Regional Modeling System for Aerosols and Deposition (REMSAD) - REMSAD was designed to calculate the concentrations of both inert and chemically reactive pollutants by simulating the physical and chemical processes in the atmosphere that affect pollutant concentrations over regional scales. It includes those processes relevant to regional haze, particulate matter and other airborne pollutants, including soluble acidic components and mercury.
Urban Airshed Model Variable Grid (UAM-V ®) - The UAM-V Photochemical Modeling System was a pioneering effort in photochemical air quality modeling in the early 1970s and has been used widely for air quality studies focusing on ozone. It is a three-dimensional photochemical grid model designed to calculate the concentrations of both inert and chemically reactive pollutants by simulating the physical and chemical processes in the atmosphere that affect pollutant concentrations. This model is typically applied to model air quality "episodes" - periods during which adverse meteorological conditions result in elevated ozone pollutant concentrations.

## Slide 16: Community Multiscale Air Quality (CMAQ)
The primary goals for the Models-3/Community Multiscale Air Quality (CMAQ) modeling system are to improve 1) the environmental management community's ability to evaluate the impact of air quality management practices for multiple pollutants at multiple scales and 2) the scientist’s ability to better probe, understand, and simulate chemical and physical interactions in the atmosphere. The latest Models-3/CMAQ version is available for download from the CMAS Website: http://www.epa.gov/asmdnerl/CMAQ/index.html

## Slide 18: Comprehensive Air quality Model with extensions (CAMx) http://www.camx.com/
The Comprehensive Air quality Model with extensions (CAMx) is a publicly available open-source computer modeling system for the integrated assessment of gaseous and particulate air pollution. CAMx is designed to
  Simulate air quality over many geographic scales
  Treat a wide variety of inert and chemically active pollutants:
    Ozone
    Inorganic and organic PM2.5/PM10
    Mercury and toxics
  Provide source-receptor, sensitivity, and process analyses
  Be computationally efficient and easy to use
The U.S. EPA has approved the use of CAMx for numerous ozone and PM State Implementation Plans throughout the U.S, and has used this model to evaluate regional mitigation strategies.
CAMx is also used throughout the world to support a wide variety of research and regulatory activities.
CAMx is written in Fortran and is designed for platforms running Unix/Linux, including Apple Mac OSx. The build scripts provided with CAMx do not support Windows/DOS.

## Slide 19: REMSAD Regional Modeling System
http://remsad.saintl.com/
The Regional Modeling System for Aerosols and Deposition (REMSAD) was developed by ICF International/Systems Applications International to support a better understanding of the distributions, sources, and removal processes relevant to regional haze, particulate matter and other airborne pollutants, including soluble acidic components and toxics.
REMSAD includes the streamlined micro-CB gas-phase chemical mechanism and an efficient transport algorithm that allow continental scale simulations of full calendar years.
REMSAD provides spatially and temporally resolved air concentrations and (wet and dry) deposition values.
Recent improvements to the modeling system include expanded treatment of mercury chemistry, the addition of a detailed secondary organic aerosol (SOA) treatment and improved performance under stagnant meteorological conditions.

## Slide 20: UAM-V® Photochemical Modeling System http://uamv.saintl.com/
The Urban Airshed Model® (UAM®) modeling system, developed and maintained by Systems Applications International (SAI), is the most widely used photochemical air quality model in the world today.
Since SAI's pioneering efforts in photochemical air quality modeling in the early 1970s, the model has undergone nearly continuous cycles of application, performance evaluation, update, extension, and improvement.

## Slide 21: Receptor Modeling
Receptor models are observational techniques which use the chemical and physical characteristics of gases and particles measured at source and receptor to both identify the presence of and to quantify source contributions to receptor concentrations.
Receptor models are mathematical or statistical procedures for identifying and quantifying the sources of air pollutants at a receptor location.
Unlike photochemical and dispersion air quality models, receptor models do not use pollutant emissions, meteorological data and chemical transformation mechanisms to estimate the contribution of sources to receptor concentrations.
Instead, receptor models use the chemical and physical characteristics of gases and particles measured at source and receptor to both identify the presence of and to quantify source contributions to receptor concentrations.
These models are therefore a natural complement to other air quality models and are used as part of State Implementation Plans (SIPs) for identifying sources contributing to air quality problems.
The EPA has developed
  the Chemical Mass Balance (CMB) and
  UNMIX models as well as the
  Positive Matrix Factorization (PMF) method for use in air quality management

## Slide 22: Available Receptor Models
Chemical Mass Balance (CMB) - The EPA-CMB Version 8.2 uses source profiles and speciated ambient data to quantify source contributions. Contributions are quantified from chemically distinct source-types rather than from individual emitters. Sources with similiar chemical and physical properties cannot be distinguished from each other by CMB.
UNMIX - The EPA UNMIX model “unmixes” the concentrations of chemical species measured in the ambient air to identify the contributing sources. Chemical profiles of the sources are not required, but instead are generated internally from the ambient data by UNMIX, using a mathematical formulation based on a form of factor analysis. For a given selection of species, UNMIX estimates the number of sources, the source compositions, and source contributions to each sample.
Positive Matrix Factorization (PMF) - The PMF technique is a form of factor analysis where the underlying co-variability of many variables (e.g., sample to sample variation in PM species) is described by a smaller set of factors (e.g., PM sources) to which the original variables are related. The structure of PMF permits maximum use of available data and better treatment of missing and below-detection-limit values.